## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26177
Problem Statement Title - A deployable AI-powered autonomous drone that aids search-and-rescue operations by detecting people and hazards, thereby improving responder safety and reducing victim discovery time.
Theme - Robotics and Drones
PS Category - Hardware
Team ID - [Enter Team ID]
YUKTI Registration ID - [Enter YUKTI ID]
Team Name - Swarm Robotics

## Slide 2
AI-Powered Autonomous SAR Drone
Proposed Solution & Technical Innovation
settings_suggestPROPOSED SOLUTION
A GPS-denied autonomous drone that enters an unmapped interior, maps it while flying, and detects both people and hazards on board.
Position comes from onboard lidar scan-matching instead of GPS, so it holds station and returns geolocated victim coordinates where satellites cannot reach. Validated end-to-end in simulation.
gavelPROBLEM SOLVED
radarAutonomous Search: Plans its own route to unexplored space. No pilot, no waypoints, no prior map of the building.
emergencyGeolocated Victims: Pinned in map coordinates: 3 of 4 survivors located, worst error 0.50 m, best 0.10 m.
shieldHazards Mapped First: 13 hazards mapped in the same run: 9 debris-narrowed passages and 4 routes with no way through.
psychologyINNOVATION
gps_offGPS-Denied Flight: Lidar odometry drives the autopilot's own EKF as a vision source, so the aircraft flies with the satellites switched off.
cell_towerCoordination Without Radio: Two drones divide the building before entry and merge results after exit, exchanging nothing in flight, because walls kill the link.
Swarm Robotics

## Slide 3: TECHNICAL APPROACH
Swarm Robotics
Technologies to be used
developer_boardHardware
Quadrotor airframe, 360-sample 2D LiDAR (12 m), aligned RGB + depth camera, IMU and barometer, and an onboard edge compute module. Thermal imaging is the planned hardware addition.
codeSoftware & Frameworks
ROS 2 Jazzy, ArduPilot (EKF3 on external navigation), Gazebo Harmonic, Python and C++, LiteRT / TensorFlow Lite SSD-Lite, OpenCV, slam_toolbox, Micro-XRCE-DDS.
Methodology and process for implementation
01
Phase 1 - Autonomy (Done)
GPS-denied flight, SLAM mapping, onboard detection and self-directed frontier search, flown unattended from arm to landing.
02
Phase 2 - Two Drones (Done)
Sector partitioning assigned before entry, plus hazard mapping and a ground station that merges both drones into one report.
03
Phase 3 - Hardware
Port the same ROS 2 graph onto a physical airframe with edge compute and add a thermal camera for smoke and low-light conditions.
04
Phase 4 - Field Trials
Validate flight stability, detection accuracy and latency in disaster-simulation conditions with rescue practitioners.

## Slide 4: FEASIBILITY AND VIABILITY Analysis, Potential Challenges & Strategic Mitigations
analyticsFEASIBILITY ANALYSIS
verifiedWorking Prototype: A complete mission already runs unattended: arm, search, detect, report, return, land. The results below are measured, not projected.
buildCOTS + Open Source: ROS 2 and ArduPilot on commodity hardware. Nothing in the software graph is simulation-specific, so the same stack flies the airframe.
warningCHALLENGES & RISKS
battery_alertBattery Constraints: Restricted flight endurance limits how much of a structure a single sortie can cover.
wifi_offRadio Denial Indoors: Reinforced concrete costs 10-20 dB per wall, so drones cannot depend on a live link to each other or to the operator.
timelineOdometry Drift: Scan-matching accumulates error over a long flight, which moves every coordinate the drone reports.
gavelMITIGATION STRATEGIES
battery_charging_fullPower Management: Hot-swappable packs, and a search that splits across drones so each sortie covers less ground.
hubBoundary Coordination: Sectors are agreed before entry and results reconciled after exit, so no in-flight radio link is required at all.
exploreLiDAR Navigation (Built): Implemented and flown. Survivor coordinates land within 0.50 m of ground truth across a 26 m building, with no satellite fix.
Swarm Robotics

## Slide 5: IMPACT AND BENEFITS Potential Target Audience Impact & Key Strategic Benefits
groupsTARGET AUDIENCE IMPACT
securityFirst Responders: The floor plan, the victim coordinates and the hazards all arrive before anyone enters. Narrowed passages and dead routes are marked in advance.
healingVictims: Protects the golden hour: two drones halve the ground each has to cover, and every confirmed victim arrives as a coordinate a responder can walk to.
starBENEFITS OF THE SOLUTION
publicSocial: Preserves life in earthquakes, building collapses, industrial accidents and missing-person searches, including where no radio or satellite reaches.
paymentsEconomic: Cuts the manpower and hours a prolonged manual sweep demands, and is built on commodity hardware and open-source software.
ecoEnvironmental: An electric UAV carries a far smaller carbon and noise footprint than the rescue helicopters it supplements.
Swarm Robotics

## Slide 6: RESEARCH AND REFERENCES Key Academic & Technical Literature Supporting the Solution
memoryOn-Device Inference
LiteRT / TensorFlow Lite SSD-Lite object detection, running CPU-only inside an edge compute budget with no cloud dependency.
travel_exploreFrontier-Based Exploration
B. Yamauchi, 'A Frontier-Based Approach for Autonomous Exploration', IEEE CIRA 1997. The basis of the drone's self-directed search.
flightGPS-Denied Flight Control
ArduPilot EKF3 external-navigation sources and the AP_DDS native ROS 2 interface, used to fly on vision instead of GPS.
mapSLAM and Laser Odometry
S. Macenski, slam_toolbox (JOSS 2021), and M. Jaimez et al., 'Planar Odometry from a Radial Laser Scanner' (RF2O), ICRA 2016.
Swarm Robotics